## Slide 1: Site Sensing and Data Mining for Construction Performance Improvement
Carlos H. Caldas, Ph.D., PE
Department of Civil, Architectural and Environmental Engineering
The University of Texas at Austin

## Slide 2: Agenda
Real-Time Spatial Information Acquisition and Use
Image-Based Safety Assessment
Materials Tracking
Video Analysis for Productivity Measurement
Semi-Automated Activity Analysis

## Slide 3: Real-Time Spatial Information Acquisition and Use
Acknowledgement: My Former Ph.D. Student
Dr. Jochen Teizer
Former Associate Professor
Georgia Institute of Technology, USA

## Slide 4
Real-Time Spatial Information Acquisition and Use for Infrastructure Construction and Maintenance
This project developed methods of acquiring, integrating, modeling, and analyzing project site spatial data, including dynamic site information (motion of personnel and equipment), that allow scalability and robustness for real-time field deployment and with sufficient accuracy for applications such as real-time safety monitoring, productivity studies, and advanced equipment control.
(NSF Award Number: CMS 0409326)

## Slide 5: Motivation
Need for safety in construction/infrastructure:
  1224 fatalities in 2005
  Many accidents occur while operating heavy equipment
Analysis of Fatalities on Construction Sites (OSHA, 2002)

## Slide 6: Motivation
Development of active safety features using 3D data
  reduce the likelihood of accidents such as
Collision of heavy equipment with people (OSHA, 2003)
Collision of heavy equipment with power line (OSHA, 2003)
“Create virtual safety nets for job sites”

## Slide 7
  Detect and track static and moving objects from a static or moving sensor
  Develop robust real-time processing algorithms
  Verify/validate via experiments (indoor and outdoor)
    Objects’ position
    Objects’ dimensions
    Objects’ direction of movement
    Objects’ velocity
Research Objectives

## Slide 8
Static Box Human walking Bicyclist
Real-Time 3D Imaging
Detecting and tracking moving objects in real-time
3D Range Sensor

## Slide 9
Overview of the Modeling Approach

## Slide 10
At occupancy grid size of 0.1m
Results

## Slide 11
Work Zone Safety
Source: Teizer et al., 2005, Leica HDS Inc., Audi AG
OSHA, 2002
Bernold et al., 2003
Kim et al., 2003
Applications
Integrated Vehicle-Based
Safety Systems (IVBSS)
US DOT, 2004
Audi and Continental (TEMIC), 2005
DaimlerChrysler (DSRC), 2005

## Slide 12: Image-Based Safety Assessment
Acknowledgement: My Former Ph.D. Student
Dr. Seokho Chi
Assistant Professor
Seoul National University, Korea

## Slide 13: Motivation
Safety first!
  U. S. Occupational Safety and Health Administration emphasized “Employers are responsible for preventing workers with a safe working environment.” (Wilson and Koehn, 2000)
Advances in technologies for safety improvement
  Construction resource detection and tracking
  Workspace 3D sensing and modeling
  …
   Support automated and informative safety decision making

## Slide 14: Research Objectives
Design an error impact analysis testbed for image-based safety assessment
  To model data collection and data processing errors
  To analyze the impact of the errors for safety assessment
Steps
  Identify data needs for spatial safety assessment
  Analyze image-based data collection devices and algorithms
  Develop safety rules based on spatial data
  Conduct error impact analysis using these safety rules

## Slide 15
SPATIAL SAFETY RISK FACTORS
(1) Excessive operation speed
(2) Dangerous access to unstable piles, unstable grounds, berms, and road edges
(3) Inadequate clearance and limited visibility
Safety Regulations & Best Practices
SPATIAL DATA NEEDS
(1) Moving speed
(2) Proximity to dangerous areas
(3) Stopping distance and
Proximity between objects
SOURCES
Fatality investigation reports
Operation safety handbooks
Industrial experts’ opinions
EXAMPLES
“Operators should follow the speed limit”
“Hazard areas should be marked with a warning against entry”
“Stopping distances should be maintained between heavy machinery”
(NIOSH, 1998; NIOSH, 2001; MSHA, 1999; MSHA, 2001)
Data Needs for Safety Assessment

## Slide 16: Object Identification
Object identification using stereo vision camera

## Slide 17: Object Tracking
Object tracking using stereo vision camera

## Slide 18: Safety Rules Determination
SPATIAL DATA NEEDS
(1) Moving speed
(2) Proximity to dangerous areas
(3) Stopping distance and
Proximity between objects
VIOLATION TYPES TO BE MONITORED
(1) Speed limit violation
(2 ) Access violation to dangerous areas
(3) Close proximity violation

## Slide 19: Safety Rules Determination
Safety rule: Close proximity violations
  “A close proximity violation occurs when the proximity between heavy machinery is smaller than their stopping distances.” (Oloufa et al., 2003; Riaz et al., 2006)

## Slide 20: Testbed: Internal Processing
Original Trajectory
Revised Trajectory
Random
Tracking Error Generator
(0% ~ 30%)
Original Classification
1st image: Loader
2nd image: Loader
3th image: Loader
4th image: Loader
Random Identification Error Generator
(0% ~ 30%)
Revised Classification
1st image: Loader
2nd image: Truck
3th image: Loader
4th image: Loader
Error Impact Analysis

## Slide 21: Testbed: Internal Processing
Safety rule for violation detection
Different time interval (0~5sec) for violation detection
1-second interval
frame-by-frame
Revised Trajectory & Classification Information
Safety Rule
Safety Decision
Violate or not?
Detected Violation
at 7 second: speed limit
at 7.5 second: none
at 8 second: speed limit
at 8.5 second: speed limit
at 9 second: speed limit
# of violation detected: 4
# of violation detected: 1
Error Impact Analysis

## Slide 22: Testbed: Output Data
Movie file showing simulated scenario
Trajectory with different tracking error rates
Error Impact Analysis
0%
4%
10%

## Slide 23: Materials Tracking
Acknowledgement: My Former Ph.D. Student
Dr. David Grau
Assistant Professor
Arizona State University, USA

## Slide 24: Motivation
Manual collection of site data is error-prone, inefficient, and expensive (Sacks 2003; Ergen 2007)
Workers spend large amounts of their time either searching or waiting for components (Rojas 2003; Caldas 2006)
The inability to locate needed items negatively affects installation productivity (CII 1986; Thomas 1989; CII 1999)
Construction activities require constant visibility for proper control (Stone 1995; Hwang 2004; Fiatech 2008)
Previous studies determined that information technologies have a great potential to improve site tracking processes (Vorster and Lucko 2002)

## Slide 25: Research Objectives
To develop a model for the automated identification and localization of construction components on large industrial projects, and
To assess/validate the impact of the automated identification and localization approach on a construction job site

## Slide 26: Research Scope
The focus of this study is on the automated identification and location of construction components on industrial sites
Job Site
Supply Chain Process

## Slide 27
Large industrial projects:
Extensive lay down yards far from installation areas
Thousands of engineered components
Research Scope
Notes: Change picture

## Slide 28: Localization Approach
A worker equipped with GPS and RFID receivers identifies tagged components around the his/her own GPS position
These receivers could also be installed on
construction equipment (e.g. cranes)

## Slide 29
Uncertainty of tags location is reduced from (a) the RFID read area to (b) much smaller areas by localization algorithms
(a) Original uncertainty area ≈30,000m2
(b) Reduced uncertainty area ≈ 40m2
Localization Approach

## Slide 30
Model Schema
Localization Model

## Slide 31
Senses, collects, and stores the worker’s GPS positions and the unique RFID identification codes
Sensor synchronization
Data fusion
Data Collection Module

## Slide 32: Location Estimation Module
Centroid Algorithms
For a given tag, its estimated location is the centroid of the K GPS positions where the tag was identified
Positions weighted according to the RFID signal strength
Localization error
0 db - Max. signal strength
-90db - Min. signal strength
Signal Strength

## Slide 33: Location Estimation Module
Proximity Algorithms
It assumes an square RFID signal pattern of side ρ
For a given tag, the four GPS positions situated at axis extremes (maximum and minimum X and Y) determine the smallest uncertainty area
Localization error

## Slide 34: Navigation Module
Mapping/navigation functions
Integration of GIS (Geographic Information Systems) and real-time differentially corrected GPS
Alternatively, printed maps can enable navigation

## Slide 35: Field Trial
The project:
CII RT240 “Leveraging Technology to Improve Construction Productivity”
  University of Waterloo; University of Kentucky; University of Texas
Coal power plant project, Rockdale, TX
$900 million
650 MWatts
Open job
Two almost identical boiler support steel structures

## Slide 36
Methodology:
Comparision of labor and productivity records between similar boiler installation sequences of tagged and non-tagged steel components
Field Trial

## Slide 37: Lay Down Yard Navigation
Detail Page 3
MWR Map

## Slide 38: Staging Area Navigation
Staging Map
Detail Page 1
List of mapped components

## Slide 39: Results - Craft Work Hours
Current process:
494 sec (8.2 min)
per component
Automated process:
195 sec (3.2 min)
per component
2.5 productivity ratio

## Slide 40: Lost components
10% of untagged components (35/366) not immediately found
0.5% of tagged components (2/366) not immediately found
Extra time required to find these “lost” components

## Slide 41: Predictability
Searching and flagging times:
Untagged Components
  Median: 301 sec (5.1 min)
  Maximum: 1,150 sec (9.2 min)
  Minimum: 131 sec (2.2 min)
Tagged Components
  Median: 124 sec (2.1 min)
  Maximum: 450 sec (7.5 min)
  Minimum: 50 sec (0.8 min)

## Slide 42: Video Interpretation For Productivity Measurement
Acknowledgement: My Former Ph.D. Student
Dr. Jie Gong
Assistant Professor
Rutgers University, USA

## Slide 43: Motivation
Low construction productivity
  49.6% of craft hour hours devoted to non-value added activities (Horman and Kenley 2005)
(Gong, Borcherding, and Caldas, 2011)

## Slide 44: Motivation
Issues with current productivity measurement methods:
  Extensive manual work (Navon 2007; Hildreth et al. 2005)
  Error-prone and expensive (Navon and Sacks 2007)

## Slide 45: Research Objectives
Formalize a computational representation of the process of video-based productivity analysis.
Design mechanisms of leveraging prior construction knowledge to assist productivity-oriented video reasoning.
Characterize and integrate a set of computing methods to support the recognition and tracking of construction resources.

## Slide 46: Proposed Video Interpretation Methodology

## Slide 47: Visual Recognition and Tracking
Method Productivity Delay Model
The time between consecutive occurrences of the production unit
The most basic or fundamental resource
An amount of work that can easily be visually measured
Column Pour
Production Unit = Concrete Bucket
The Method’s Leading Resource = Concrete Bucket
Sample Case
Adrian (1974)
Leverage domain knowledge to determine which object to recognize and track

## Slide 48: Model-Based Reasoning – Formal Steps
State Classification
  Definition: Object status in predetermined categories
  Example: <<waiting>>, <<working>>
Event Detection
  Definition: Change of states
  Example: <<waiting  working>>
Scenario Recognition
  Definition: A situation inferred according to a predetermined rule sets
  Example: <<process violation>>
Time Utilization
Workflow
Abnormal Scenario
Reasoning Steps
What to measure?

## Slide 49: Model-Based Reasoning – Representing Prior Knowledge
  Semantic Context
    Task elements
  Spatial Context
    Spatial layout
    Work zones
  Temporal Context
    Activity sequences
    Time constrains
Bucket Ready Zone
Bucket Pour Zone
Process Model
or
Process Chart

## Slide 50: Video Content Organization and Retrieval

## Slide 51: Implementation of Video Interpretation Methodology
  VC++ Microsoft Foundation Class (MFC)
  Intel Open Source Computer Vision Library
  DirectShow

## Slide 52: Validation Cases
Repetitive Operations
  Column Pour Operation
  Slab Pour Operation
  Earthmoving Operation
Non-Repetitive Operations
  Scaffold Installation
  Hoisting Operation

## Slide 53: Demonstration – Column Pour

## Slide 54: Analysis of Processing Results
Manual
Computer

## Slide 55
Analysis of Processing Results
Time Constrain Violation
Sequence Violation
Overall Time Utilization Accuracy: 90%

## Slide 56: Semi-Automated Activity Analysis
Acknowledgement: My Former Ph.D. Student
Jung Yeol Kim, Ph.D.
Assistant Professor
Inha University, Korea

## Slide 57: Activity Analysis
Definition
  “A continuous process of measuring and increasing the amount of time that craft professionals spend on actual construction” (CII 2010b, iii).
  Activity Analysis is an evolution of Work Sampling
Data Gathering: Manual Observation
Direct Work
Preparatory Work
Tools and Equip.
Material Handling
Waiting
Travel
Personal
Maximize
Optimize
others

## Slide 58: Semi-Automated Activity Analysis
Plan Study
Sample
Analyze
Plan Improvements
Implement Improvements
Semi-automated Data Collection
Activity Analysis Process
Research Scope
Automated Data Analysis
Kim, J. Y. (2015) “Rapid and Contextual Activity Analysis: A Semi-automated Activity Category, Time, Location, and Video Data Collection and Analysis Methodology”. PhD Dissertation. University of Texas at Austin

## Slide 59: Semi-Automated Activity Analysis
Kim, J. Y. (2015) “Rapid and Contextual Activity Analysis: A Semi-automated Activity Category, Time, Location, and Video Data Collection and Analysis Methodology”. PhD Dissertation. University of Texas at Austin

## Slide 60: Integrated Data Collection
<Integrated Data Structure>
Kim, J. Y. (2015) “Rapid and Contextual Activity Analysis: A Semi-automated Activity Category, Time, Location, and Video Data Collection and Analysis Methodology”. PhD Dissertation. University of Texas at Austin

## Slide 61: Integrated Data Analysis
<Sequence Diagram of Data Analysis>
Kim, J. Y. (2015) “Rapid and Contextual Activity Analysis: A Semi-automated Activity Category, Time, Location, and Video Data Collection and Analysis Methodology”. PhD Dissertation. University of Texas at Austin

## Slide 62: Dynamic Analysis
Kim, J. Y. (2015) “Rapid and Contextual Activity Analysis: A Semi-automated Activity Category, Time, Location, and Video Data Collection and Analysis Methodology”. PhD Dissertation. University of Texas at Austin

## Slide 63: Dynamic Analysis
Kim, J. Y. (2015) “Rapid and Contextual Activity Analysis: A Semi-automated Activity Category, Time, Location, and Video Data Collection and Analysis Methodology”. PhD Dissertation. University of Texas at Austin

## Slide 64: Case Studies
Kim, J. Y. (2015) “Rapid and Contextual Activity Analysis: A Semi-automated Activity Category, Time, Location, and Video Data Collection and Analysis Methodology”. PhD Dissertation. University of Texas at Austin

## Slide 65: Final Thoughts
Site sensing and data analysis provide opportunities for construction performance improvement in many areas.
Commercial applications have been developed, but many research challenges still need to be addressed.
We are continuing our journey to make research contributions that eventually will enable the development of fully integrated and automated project processes.

## Slide 66: Thank you!
Carlos H. Caldas, Ph.D., PE
Department of Civil, Architectural and Environmental Engineering
The University of Texas at Austin
caldas@mail.utexas.edu